If the paver is being operated under automatic grade and slope control, the screed operator should not attempt to change the angle of attack of the screed by turning the thickness control cranks. The automatic controls will correct any changes made in the angle of attack of the screed by changing the position of the tow point where the screed is attached to the tractor in order to reestablish the original screed angle.